## Slide 1
WEEKLY STANDUP
LoRaWAN weekly standup,
UG65 + Dragino work,
and future plans
This week's Milesight UG65 and Dragino work,
technical detail, and future prototype assembly.
Jervis James Pedotim | Intern | 02 Aug 2026
Technology stack
Notes: [Sources]
- presentation/STANDUP_PRESENTATION_DECK.md
- Presentation logo assets under presentation/
[/Sources]

## Slide 2
WEEKLY STANDUP / INTERN LEARNING
This week I worked with a Milesight UG65 and Dragino sensor
02 / 18
lorawan-setup
Weekly standup
This week's work followed one real sensor uplink through the local stack, from gateway radio reception to application integrations.
WORK COMPLETED
-
Connected the UG65 to Gateway_F94C0B and used 192.168.23.150 as the gateway endpoint.
-
Ran the Ubuntu VM at 192.168.23.137 and forwarded Semtech UDP traffic on port 1700.
-
Registered the Dragino LSN50v2-S31 with OTAA and verified Class A uplink behavior.
-
Matched the JavaScript decoder to TempC_SHT31, Hum_SHT31, and BatV fields.
RESULT
A complete
uplink path
The same event can be traced through RF, UDP, MQTT,
ChirpStack, PostgreSQL, Grafana, and Node-RED.
Notes: [Sources]
- docs/README.md
- docs/01-master-deployment-guide.md
- docs/02-offline-direct-ap-setup-guide.md
- docs/03-postgres-integration-guide.md
- docs/04-grafana-integration-guide.md
- docs/05-node-red-integration-guide.md
- docs/06-lorawan-rf-security-toolkit-brief.md
- docs/07-lorawan-rf-and-protocol-testing-setup-guide.md
- docs/08-lorawan-security-testing-runbook.md
- docs/09-rak5146-wisblock-gateway-commissioning-manual.md
[/Sources]

## Slide 3
WEEKLY STANDUP / INTERN LEARNING
The test was checked at each handoff
03 / 18
lorawan-setup
Weekly standup
A dashboard value is only useful when the packet, device state, decoder, and downstream records agree.
VERIFICATION POINTS
-
Gateway RF — the UG65 receives the Dragino uplink.
-
UDP transport — the packet reaches the server on port 1700.
-
MQTT event — Gateway Bridge publishes the gateway event.
-
Application data — decoded values appear in SQL, Grafana, and Node-RED.
EVIDENCE
Uplink checks
Compare RF metadata, decoded fields, database rows, dashboard values, and flow messages.
Notes: [Sources]
- docs/README.md
- docs/01-master-deployment-guide.md
- docs/02-offline-direct-ap-setup-guide.md
- docs/03-postgres-integration-guide.md
- docs/04-grafana-integration-guide.md
- docs/05-node-red-integration-guide.md
[/Sources]

## Slide 4
WEEKLY STANDUP / INTERN LEARNING
This week's test traced one Dragino uplink end to end
04 / 18
lorawan-setup
Weekly standup
The path was Dragino sensor -> Milesight UG65 -> Gateway Bridge -> MQTT -> ChirpStack -> PostgreSQL, Grafana, and Node-RED.
Dragino LSN50v2-S31
uplink
->
Milesight UG65
RF to IP
->
Gateway Bridge
UDP 1700
->
MQTT
event bus
->
ChirpStack
OTAA + decode
->
Apps
SQL + dashboards + flows
TRACEABILITY
Check RF, UDP, MQTT, server state, decoded fields, and application output independently.
Notes: [Sources]
- docs/README.md
- docs/01-master-deployment-guide.md
- docs/03-postgres-integration-guide.md
- docs/04-grafana-integration-guide.md
- docs/05-node-red-integration-guide.md
[/Sources]

## Slide 5
WEEKLY STANDUP / INTERN LEARNING
LoRa radio and LoRaWAN have different responsibilities
05 / 18
lorawan-setup
Weekly standup
The UG65 receives LoRa radio traffic. LoRaWAN defines how the Dragino joins, sends uplinks, and receives Class A downlinks.
LoRa = physical layer
-
Chirp Spread Spectrum radio carries low-power long-range links.
-
Spreading factor, bandwidth, coding rate, and frequency affect the link budget.
-
The UG65 receives RF and forwards packets; it does not decide application meaning.
LoRaWAN = network layer
-
LoRaWAN defines activation, frame counters, classes, and regional parameters.
-
OTAA establishes session state; keys and identifiers must match the server profile.
-
The Dragino is Class A; downlinks wait for its receive window after an uplink.
LoRa carries the signal; LoRaWAN defines device identity, security, and network behavior.
Notes: [Sources]
- docs/01-master-deployment-guide.md
- docs/06-lorawan-rf-security-toolkit-brief.md
- docs/07-lorawan-rf-and-protocol-testing-setup-guide.md
[/Sources]

## Slide 6
WEEKLY STANDUP / INTERN LEARNING
The gateway and server perform different jobs
06 / 18
lorawan-setup
Weekly standup
The UG65 does not decode application data, and ChirpStack does not replace the gateway radio. They meet at the packet-forwarder boundary.
Milesight UG65
-
Receives LoRa frames from the Dragino over the configured regional channels.
-
Adds gateway metadata and forwards packets over IP.
-
Does not own OTAA application state or payload meaning.
ChirpStack v4
-
Receives gateway events through Gateway Bridge.
-
Validates gateway, device profile, OTAA state, and frame counters.
-
Decodes payload bytes and publishes normalized events.
Troubleshoot RF and UDP separately from device state and payload decoding.
Notes: [Sources]
- docs/01-master-deployment-guide.md
- docs/02-offline-direct-ap-setup-guide.md
- docs/06-lorawan-rf-security-toolkit-brief.md
[/Sources]

## Slide 7
WEEKLY STANDUP / INTERN LEARNING
ChirpStack validates, decodes, and publishes the uplink
07 / 18
lorawan-setup
Weekly standup
Gateway Bridge passes the UG65 packet to ChirpStack v4. The server checks state, applies the codec, and publishes the decoded event.
1. Ingest
-
Receives packets forwarded by the Milesight UG65.
-
Associates frames with the gateway and Dragino device.
-
Tracks radio metadata such as RSSI and SNR.
2. Validate
-
Checks region, device profile, and OTAA state.
-
Verifies security state and frame-counter behavior.
-
Applies Class A downlink timing rules.
3. Decode + publish
-
Runs the Dragino JavaScript payload codec.
-
Exposes temperature, humidity, and battery fields.
-
Publishes decoded events for SQL, dashboards, and flows.
ChirpStack is the protocol and device-state boundary between the gateway and the applications.
Notes: [Sources]
- docs/01-master-deployment-guide.md
- docs/configs/chirpstack.toml
- docs/configs/chirpstack-gateway-bridge.toml
- docs/codecs/dragino-lsn50v2-s31-decoder.js
[/Sources]

## Slide 8
WEEKLY STANDUP / INTERN LEARNING
The decoder maps payload bytes to named fields
08 / 18
lorawan-setup
Weekly standup
The Dragino payload is binary at the radio layer; the JavaScript codec maps byte positions into application values.
Decoder inputs
-
Raw FRMPayload bytes from the uplink.
-
FPort and device profile select the codec.
-
Frame metadata remains beside the payload.
Decoded outputs
-
TempC_SHT31 — temperature from the SHT31 probe.
-
Hum_SHT31 — relative humidity from the SHT31 probe.
-
BatV — battery voltage for device health.
A wrong decoder or profile can create plausible but incorrect dashboard values.
Notes: [Sources]
- docs/01-master-deployment-guide.md
- docs/02-offline-direct-ap-setup-guide.md
- docs/03-postgres-integration-guide.md
- docs/codecs/dragino-lsn50v2-s31-decoder.js
[/Sources]

## Slide 9
WEEKLY STANDUP / INTERN LEARNING
The direct AP setup isolated the local test network
09 / 18
lorawan-setup
Weekly standup
The UG65 exposed Gateway_F94C0B. The VM used a static address and the gateway forwarded packets to the server over UDP 1700.
Ubuntu VM
-
Bridged Wi-Fi linked the VM to the UG65 access point.
-
VM address: 192.168.23.137/24.
-
Gateway route: 192.168.23.150.
Docker Compose
-
Runs ChirpStack, Gateway Bridge, MQTT, PostgreSQL, and Redis.
-
Volumes retain service state.
-
Stage images before offline use.
Operational network
-
Gateway: 192.168.23.150.
-
Semtech UDP: 1700.
-
MQTT event transport: TCP 1883.
The Dragino reached the local server without cloud connectivity.
Notes: [Sources]
- docs/01-master-deployment-guide.md
- docs/02-offline-direct-ap-setup-guide.md
- docs/configs/docker-compose.yml
- docs/configs/chirpstack-gateway-bridge.toml
[/Sources]

## Slide 10
WEEKLY STANDUP / INTERN LEARNING
PostgreSQL stores decoded telemetry and radio evidence
10 / 18
lorawan-setup
Weekly standup
The integration database keeps decoded fields and packet metadata available for SQL queries, dashboards, and later analysis.
Data model
-
Dedicated chirpstack_integration database for event history.
-
JSONB stores decoded payloads without forcing one rigid sensor schema.
-
SQL views expose stable fields for dashboards and reports.
What becomes measurable
-
Dragino values: TempC_SHT31, Hum_SHT31, and BatV.
-
Radio quality: RSSI, SNR, timing, and gateway metadata.
-
Operational evidence: joins, acknowledgements, and status events.
The database is the durable record of the uplink.
Notes: [Sources]
- docs/03-postgres-integration-guide.md
- docs/README.md
- docs/configs/chirpstack.toml
[/Sources]

## Slide 11
WEEKLY STANDUP / INTERN LEARNING
Grafana turns stored telemetry into readable views
11 / 18
lorawan-setup
Weekly standup
Grafana reads PostgreSQL data to show current values, time-series changes, thresholds, and comparisons across sensors.
Latest values
-
Gauges show latest decoded values.
-
Thresholds highlight values that need attention.
-
One dashboard can compare sensors later.
Time series
-
SQL queries reveal trends rather than isolated readings.
-
$__timeFilter keeps panels on the selected range.
-
Variables reuse one dashboard across sensors.
Operational value
-
Compare zones and time windows.
-
Use alerts before manual inspection.
-
Export dashboard JSON for reuse.
Grafana summarizes telemetry; PostgreSQL remains the source for analysis.
Notes: [Sources]
- docs/04-grafana-integration-guide.md
- docs/03-postgres-integration-guide.md
- presentation/grafana.webp
[/Sources]

## Slide 12
WEEKLY STANDUP / INTERN LEARNING
Node-RED routes decoded events into rules and actions
12 / 18
lorawan-setup
Weekly standup
The flow subscribes to MQTT, normalizes fields, checks conditions, and prepares an alert, webhook, or downlink.
Subscribe
MQTT wildcard topics
receive uplinks
->
Transform
Function nodes
normalize payloads
->
Decide
Switch / threshold
logic
->
Act
Webhook, alert,
or downlink
ACTUATION RULE
Keep actuation human-reviewed. Class A downlinks wait for the device receive window.
Notes: [Sources]
- docs/05-node-red-integration-guide.md
- docs/04-grafana-integration-guide.md
- docs/configs/docker-compose.yml
[/Sources]

## Slide 13
WEEKLY STANDUP / INTERN LEARNING
RF and LoRa signal analysis is planned, not implemented
13 / 18
lorawan-setup
Weekly standup
FUTURE WORK — RECEIVE-ONLY / AUTHORIZED PRIVATE LAB
The RF documents describe an SDR path for capturing IQ data, demodulating LoRa, extracting LoRaWAN fields, and comparing observations with ChirpStack records.
RF / IQ
gr-lora_sdr or SDRangel
->
PHY payload
demodulated LoRa bytes
->
LoRaWAN fields
LoRa_Craft / Scapy adapter
->
Evidence
Wireshark + captures
->
Server behavior
ChirpStack + LAF
SAFE START
-
Receive-only hardware first.
-
Synthetic identifiers and private tenant.
-
Preserve IQ, PCAP, logs, and hashes.
-
Any TX requires shielded/cabled path and approval.
Planned work; no RF analyzer has been implemented yet.
Notes: [Sources]
- docs/06-lorawan-rf-security-toolkit-brief.md
- docs/07-lorawan-rf-and-protocol-testing-setup-guide.md
- docs/08-lorawan-security-testing-runbook.md
[/Sources]

## Slide 14
WEEKLY STANDUP / INTERN LEARNING
Raspberry Pi 4 will host the future gateway prototype
14 / 18
lorawan-setup
Weekly standup
FUTURE PROTOTYPE / ASSEMBLY AND EXPERIMENTATION
Planned hardware path: Raspberry Pi 4 + compatible HAT + RAK5146 SPI AS923. The task is to mount, wire, power, and test the prototype.
Raspberry Pi 4
gateway computer
+
RAK5146 SPI
AS923 900-928 MHz concentrator
->
Private
ChirpStack
ASSEMBLY ORDER
Mount the concentrator, connect both antenna paths, use wired Ethernet first, and verify one clean packet path.
Notes: [Sources]
- docs/09-rak5146-wisblock-gateway-commissioning-manual.md
- hardware-checklist.pdf
- presentation/Raspberry-Pi-Logo-2012.png
[/Sources]

## Slide 15
WEEKLY STANDUP / INTERN LEARNING
WisBlock provides the future sensor-side prototype
15 / 18
lorawan-setup
Weekly standup
FUTURE PROTOTYPE / ASSEMBLY AND SENSOR PLAY
Start with one RAK4631 node, one RAK19007/19001 base, and one compatible sensor. Test the payload path before adding battery, solar, or cellular options.
RAK4631
MCU + LoRa radio
+
RAK19007 / 19001
WisBlock base board
+
One sensor
soil, weather, or RS485
+
Power later
battery / solar after bench test
FIRST TEST
Read one sensor, send one synthetic OTAA uplink, record the raw payload, then add the RAK-specific decoder and downstream integrations.
Notes: [Sources]
- docs/09-rak5146-wisblock-gateway-commissioning-manual.md
- hardware-checklist.pdf
- presentation/STANDUP_PRESENTATION_DECK.md
[/Sources]

## Slide 16
WEEKLY STANDUP / INTERN LEARNING
Hyperledger Fabric can store selected audit records
16 / 18
lorawan-setup
Weekly standup
FUTURE EXPLORATION / NOT IMPLEMENTED YET
Node-RED can send selected events or hashes to Fabric when a shared, tamper-evident record is required. PostgreSQL remains the detailed telemetry store.
Telemetry
full detail in SQL
->
Node-RED
select / validate event
->
Fabric
shared ledger entry
->
Audit
traceable proof
DESIGN QUESTION
Which events need shared verification, and which belong only in the telemetry database?
Notes: [Sources]
- docs/05-node-red-integration-guide.md
- presentation/STANDUP_PRESENTATION_DECK.md
- presentation/hyperledgerfabric.png
[/Sources]

## Slide 17
WEEKLY STANDUP / INTERN LEARNING
What I learned from the UG65 and Dragino work
17 / 18
lorawan-setup
Weekly standup
The work connected protocol behavior to the physical gateway, server configuration, decoder output, and application data.
01
Trace a packet
Follow one uplink from RF reception to the database and dashboard.
02
Separate responsibilities
The gateway forwards packets; ChirpStack validates state and decodes payloads.
03
Check the decoder
Confirm raw bytes, device profile, field names, and charts agree.
04
Keep the setup repeatable
Record AP settings, IP addresses, ports, logs, and timing.
Next: repeat the same trace with a second controlled sensor scenario.
Notes: [Sources]
- Synthesis of docs/01-master-deployment-guide.md through docs/09-rak5146-wisblock-gateway-commissioning-manual.md
- hardware-checklist.pdf
[/Sources]

## Slide 18
WEEKLY STANDUP / INTERN LEARNING
Future work: assemble hardware, then connect the prototype path
18 / 18
lorawan-setup
Weekly standup
Use the checklist before power-on. Assemble one gateway and one node, capture the first uplink, then connect the application path.
GATEWAY
-
RAK5146 SPI / AS923 900-928 MHz
-
Raspberry Pi 4 + compatible HAT
-
LoRa antenna + active GPS
-
Two pigtails, 5 V / 3 A, microSD, Ethernet
WISBLOCK
-
RAK4631 core + RAK19007/19001 base
-
Matching 900 MHz node antenna
-
USB-C cable + one compatible sensor
-
Battery/solar later; cellular None first
SAFE ORDER
-
Verify labels and parts
-
Attach RF paths before power
-
Use one gateway + one node
-
Capture first OTAA uplink, then integrate
NEXT STEPS
Assemble the Pi gateway -> assemble one WisBlock node -> capture the first OTAA uplink -> connect PostgreSQL / Grafana / Node-RED -> evaluate RF analyzer and Fabric paths.
Notes: [Sources]
- hardware-checklist.pdf
- docs/09-rak5146-wisblock-gateway-commissioning-manual.md
- docs/configs/chirpstack-gateway-bridge.toml
- docs/06-lorawan-rf-security-toolkit-brief.md
[/Sources]