## Slide 1
WEEKLY STANDUP
LoRaWAN experiment,
technology learning,
and prototype plans
This week's hands-on Milesight UG65 + Dragino experiment,
learning, and future prototype plans.
Jervis James Pedotim | Intern | 02 Aug 2026
Technology stack
Notes: [Sources]
- presentation/STANDUP_PRESENTATION_DECK.md
- Presentation logo assets under presentation/
[/Sources]

## Slide 2
WEEKLY STANDUP / INTERN LEARNING
This week I experimented with a Milesight UG65 and Dragino sensor
02 / 15
lorawan-setup
Weekly standup
Hands-on work focused on moving one real LoRaWAN sensor through the local stack and understanding each technical handoff.
HANDS-ON EXPERIMENT
-
Connected the Milesight UG65 in direct AP mode and traced Semtech UDP traffic.
-
Exercised a Dragino LSN50v2-S31 Class A sensor through OTAA.
-
Validated JavaScript decoding for temperature, humidity, and battery telemetry.
-
Followed the event into PostgreSQL, Grafana, and Node-RED integration paths.
EXPERIMENT FOCUS
One sensor,
one gateway,
one traceable path
Outcome: clearer RF-to-application understanding.
The experiment produced a traceable integration baseline.
Notes: [Sources]
- docs/README.md
- docs/01-master-deployment-guide.md
- docs/02-offline-direct-ap-setup-guide.md
- docs/03-postgres-integration-guide.md
- docs/04-grafana-integration-guide.md
- docs/05-node-red-integration-guide.md
- docs/06-lorawan-rf-security-toolkit-brief.md
- docs/07-lorawan-rf-and-protocol-testing-setup-guide.md
- docs/08-lorawan-security-testing-runbook.md
- docs/09-rak5146-wisblock-gateway-commissioning-manual.md
[/Sources]

## Slide 3
WEEKLY STANDUP / INTERN LEARNING
This week's experiment traced one Dragino uplink end to end
03 / 15
lorawan-setup
Weekly standup
The current path is concrete: Dragino sensor -> Milesight UG65 -> Gateway Bridge -> MQTT -> ChirpStack -> application integrations.
Dragino LSN50v2-S31
uplink
->
Milesight UG65
RF to IP
->
Gateway Bridge
UDP 1700
->
MQTT
event bus
->
ChirpStack
OTAA + decode
->
Apps
SQL + dashboards + flows
WHY THIS MATTERS
Tracing one real uplink made each protocol and service boundary easier to reason about.
Notes: [Sources]
- docs/README.md
- docs/01-master-deployment-guide.md
- docs/03-postgres-integration-guide.md
- docs/04-grafana-integration-guide.md
- docs/05-node-red-integration-guide.md
[/Sources]

## Slide 4
WEEKLY STANDUP / INTERN LEARNING
The experiment made the LoRa and LoRaWAN boundary concrete
04 / 15
lorawan-setup
Weekly standup
The UG65 receives LoRa radio traffic; LoRaWAN adds regional parameters, OTAA, Class A behavior, and device security.
LoRa = physical layer
-
Chirp Spread Spectrum radio carries low-power long-range links.
-
Spreading factor, bandwidth, coding rate, and frequency affect the link budget.
-
The UG65 receives RF and forwards packets; it does not decide application meaning.
LoRaWAN = network layer
-
LoRaWAN defines activation, frame counters, classes, and regional parameters.
-
OTAA establishes session state; keys and identifiers must match the server profile.
-
The Dragino is Class A; downlinks wait for its receive window after an uplink.
Experiment takeaway: radio reception is not the same as an accepted, decoded, actionable uplink.
Notes: [Sources]
- docs/01-master-deployment-guide.md
- docs/06-lorawan-rf-security-toolkit-brief.md
- docs/07-lorawan-rf-and-protocol-testing-setup-guide.md
[/Sources]

## Slide 5
WEEKLY STANDUP / INTERN LEARNING
ChirpStack made the Dragino uplink actionable
05 / 15
lorawan-setup
Weekly standup
The hands-on path connected the UG65 through Gateway Bridge to ChirpStack v4, then used the device profile and codec to expose telemetry.
1. Ingest
-
Receives packets forwarded by the Milesight UG65.
-
Associates frames with the gateway and Dragino device.
-
Tracks radio metadata such as RSSI and SNR.
2. Validate
-
Checks region, device profile, and OTAA state.
-
Verifies security state and frame-counter behavior.
-
Applies Class A downlink timing rules.
3. Decode + publish
-
Runs the Dragino JavaScript payload codec.
-
Exposes temperature, humidity, and battery fields.
-
Publishes decoded events for SQL, dashboards, and flows.
Experiment takeaway: one real uplink is more useful when every server-side handoff is traceable.
Notes: [Sources]
- docs/01-master-deployment-guide.md
- docs/configs/chirpstack.toml
- docs/configs/chirpstack-gateway-bridge.toml
- docs/codecs/dragino-lsn50v2-s31-decoder.js
[/Sources]

## Slide 6
WEEKLY STANDUP / INTERN LEARNING
Direct AP mode gave the UG65 experiment a controlled network
06 / 15
lorawan-setup
Weekly standup
The UG65 exposed its Gateway_F94C0B Wi-Fi AP; the VM used a static address so the local packet path stayed deterministic.
Ubuntu VM
-
VirtualBox bridged the VM to the host Wi-Fi adapter.
-
Netplan managed static/DHCP transitions.
-
VM address: 192.168.23.137/24.
Docker Compose
-
Runs ChirpStack, Gateway Bridge, MQTT, PostgreSQL, and Redis.
-
Volumes preserve state across restarts.
-
Pre-stage images for offline use.
Operational network
-
Gateway address: 192.168.23.150.
-
Semtech forwarding uses UDP 1700.
-
The packet-forwarder settings must be re-applied after a gateway reboot.
Current-week experiment: the Dragino data reached the local server without relying on cloud connectivity.
Notes: [Sources]
- docs/01-master-deployment-guide.md
- docs/02-offline-direct-ap-setup-guide.md
- docs/configs/docker-compose.yml
- docs/configs/chirpstack-gateway-bridge.toml
[/Sources]

## Slide 7
WEEKLY STANDUP / INTERN LEARNING
PostgreSQL preserved the Dragino experiment as queryable events
07 / 15
lorawan-setup
Weekly standup
The integration database turned live uplinks into durable records that I could inspect, query, and reuse in downstream tools.
Data model
-
Dedicated chirpstack_integration database for event history.
-
JSONB stores decoded payloads without forcing one rigid sensor schema.
-
SQL views expose stable fields for dashboards and reports.
What becomes measurable
-
Dragino values: TempC_SHT31, Hum_SHT31, and BatV.
-
Radio quality: RSSI, SNR, timing, and gateway metadata.
-
Operational evidence: joins, acknowledgements, and status events.
Experiment takeaway: persistence converts a live uplink into evidence I can compare and reuse.
Notes: [Sources]
- docs/03-postgres-integration-guide.md
- docs/README.md
- docs/configs/chirpstack.toml
[/Sources]

## Slide 8
WEEKLY STANDUP / INTERN LEARNING
Grafana made Dragino behavior visible beyond one packet
08 / 15
lorawan-setup
Weekly standup
Using PostgreSQL data, I explored gauges and time-series views for the Dragino telemetry.
Current state
-
Gauges show latest decoded values.
-
Color thresholds make risk visible quickly.
-
A dashboard can compare multiple sensor zones later.
Time series
-
SQL queries reveal trends rather than isolated readings.
-
The $__timeFilter macro keeps panels aligned to the selected range.
-
Variables can scale one dashboard across sensors.
Operational value
-
Operators can compare zones and time windows.
-
Alerts can point to a condition before manual inspection.
-
Dashboard JSON export makes the view portable.
Experiment takeaway: a dashboard is an interface to telemetry evidence, not the evidence itself.
Notes: [Sources]
- docs/04-grafana-integration-guide.md
- docs/03-postgres-integration-guide.md
- presentation/grafana.webp
[/Sources]

## Slide 9
WEEKLY STANDUP / INTERN LEARNING
Node-RED connected Dragino events to rules and actions
09 / 15
lorawan-setup
Weekly standup
I explored the MQTT-driven flow: receive the uplink, inspect decoded fields, apply a rule, then prepare an alert or downlink.
Subscribe
MQTT wildcard topics
receive uplinks
->
Transform
Function nodes
normalize payloads
->
Decide
Switch / threshold
logic
->
Act
Webhook, alert,
or downlink
Control point
For current experiments, keep actuation human-reviewed; Class A downlinks wait for the device's receive window.
Notes: [Sources]
- docs/05-node-red-integration-guide.md
- docs/04-grafana-integration-guide.md
- docs/configs/docker-compose.yml
[/Sources]

## Slide 10
WEEKLY STANDUP / INTERN LEARNING
RF and LoRa signal analysis is a future extension
10 / 15
lorawan-setup
Weekly standup
FUTURE WORK / NOT IMPLEMENTED YET / AUTHORIZED PRIVATE LAB ONLY
The RF documents define a future analyzer path to observe over-the-air behavior and correlate it with the local ChirpStack path.
RF / IQ
gr-lora_sdr or SDRangel
->
PHY payload
demodulated LoRa bytes
->
LoRaWAN fields
LoRa_Craft / Scapy adapter
->
Evidence
Wireshark + captures
->
Server behavior
ChirpStack + LAF
SAFE START
-
Receive-only hardware first.
-
Synthetic identifiers and private tenant.
-
Preserve IQ, PCAP, logs, and hashes.
-
Any TX requires shielded/cabled path and approval.
This is documented future work, not a completed implementation.
Notes: [Sources]
- docs/06-lorawan-rf-security-toolkit-brief.md
- docs/07-lorawan-rf-and-protocol-testing-setup-guide.md
- docs/08-lorawan-security-testing-runbook.md
[/Sources]

## Slide 11
WEEKLY STANDUP / INTERN LEARNING
The Raspberry Pi 4 gateway is a prototype assembly task
11 / 15
lorawan-setup
Weekly standup
FUTURE PROTOTYPE / ASSEMBLY AND EXPERIMENTATION
The next hardware path is a planned custom gateway for private-network experiments. My next responsibility is to assemble it, test the interfaces, and play with the prototype.
Raspberry Pi 4
gateway computer
+
RAK5146 SPI
AS923 900-928 MHz concentrator
->
Private
ChirpStack
Assembly focus
Mount the concentrator on the Pi HAT, connect both antenna paths, use wired Ethernet first, and prove one clean packet path before adding outdoor or solar complexity.
Notes: [Sources]
- docs/09-rak5146-wisblock-gateway-commissioning-manual.md
- hardware-checklist.pdf
- presentation/Raspberry-Pi-Logo-2012.png
[/Sources]

## Slide 12
WEEKLY STANDUP / INTERN LEARNING
The WisBlock node is the small field experiment
12 / 15
lorawan-setup
Weekly standup
FUTURE PROTOTYPE / ASSEMBLY AND SENSOR PLAY
Start with one node and one sensor. The purpose is to learn the payload path, power behavior, and physical assembly before scaling the field design.
RAK4631
MCU + LoRa radio
+
RAK19007 / 19001
WisBlock base board
+
One sensor
soil, weather, or RS485
+
Power later
battery / solar after bench test
First experiment
Read one sensor, send one synthetic OTAA uplink, record the raw payload, and only then add the RAK-specific decoder and downstream integrations.
Notes: [Sources]
- docs/09-rak5146-wisblock-gateway-commissioning-manual.md
- hardware-checklist.pdf
- presentation/STANDUP_PRESENTATION_DECK.md
[/Sources]

## Slide 13
WEEKLY STANDUP / INTERN LEARNING
Hyperledger Fabric can add a verifiable audit layer
13 / 15
lorawan-setup
Weekly standup
FUTURE EXPLORATION / NOT IMPLEMENTED YET
The idea is not to replace PostgreSQL. It is to use Node-RED to send selected events or hashes to Fabric when a shared, tamper-evident record is valuable.
Telemetry
full detail in SQL
->
Node-RED
select / validate event
->
Fabric
shared ledger entry
->
Audit
traceable proof
Design question for the prototype
Which events need shared verification, and which belong only in the high-volume telemetry store?
Notes: [Sources]
- docs/05-node-red-integration-guide.md
- presentation/STANDUP_PRESENTATION_DECK.md
- presentation/hyperledgerfabric.png
[/Sources]

## Slide 14
WEEKLY STANDUP / INTERN LEARNING
What the UG65 + Dragino experiment taught me
14 / 15
lorawan-setup
Weekly standup
The biggest shift was seeing one real sensor move through the full stack: radio, gateway, server, decoder, storage, and automation.
01
RF-to-application tracing
One uplink is a chain of observable handoffs, not a single dashboard event.
02
Gateway vs network server
The UG65 forwards radio traffic; ChirpStack validates device state and decodes payloads.
03
Decoder-first debugging
Raw bytes, device profile, JSONB fields, and charts must agree before data is useful.
04
Operational repeatability
AP mode, static IP, ports, logs, and downlink timing all shape the experiment.
Next confidence gain: repeat the same trace with a second controlled sensor scenario.
Notes: [Sources]
- Synthesis of docs/01-master-deployment-guide.md through docs/09-rak5146-wisblock-gateway-commissioning-manual.md
- hardware-checklist.pdf
[/Sources]

## Slide 15
WEEKLY STANDUP / INTERN LEARNING
Future plan: pass the hardware gate, then assemble
15 / 15
lorawan-setup
Weekly standup
Next phase is physical assembly and experimentation; this checklist is the last control before power-on.
GATEWAY
-
RAK5146 SPI / AS923 900-928 MHz
-
Raspberry Pi 4 + compatible HAT
-
LoRa antenna + active GPS
-
Two pigtails, 5 V / 3 A, microSD, Ethernet
WISBLOCK
-
RAK4631 core + RAK19007/19001 base
-
Matching 900 MHz node antenna
-
USB-C cable + one compatible sensor
-
Battery/solar later; cellular None first
SAFE ORDER
-
Verify labels and parts
-
Attach RF paths before power
-
Use one gateway + one node
-
Capture first OTAA uplink, then integrate
NEXT STEPS
Assemble the Pi gateway -> assemble one WisBlock node -> add the RAK decoder -> connect PostgreSQL / Grafana / Node-RED -> explore Fabric and RF analyzer paths.
Notes: [Sources]
- hardware-checklist.pdf
- docs/09-rak5146-wisblock-gateway-commissioning-manual.md
- docs/configs/chirpstack-gateway-bridge.toml
- docs/06-lorawan-rf-security-toolkit-brief.md
[/Sources]